## Slide 1: Runtime Verification Based on Executable Models: On-the-Fly Matching of Timed Traces
Mikhail Chupilko,
Alexander Kamkin

## Slide 2: Outline
Hardware models
Runtime verification
Elements of formalization
Conformance relation
Conclusion

## Slide 3: Hardware models
They are developed in Hardware Description Languages, like Verilog or VHDL
The result of development is the program being executed in HDL simulator
The common approach for verification of hardware models is testing of HDL programs
To automatize testing is possible by means of executable models (e.g. in C++)

## Slide 4: HDL programs
input S;
output R1, R2;
void design() {
while(true) {
wait(S);
delay(6);
R1 = 1;
delay(1);
R1 = 0;
R2 = 1;
delay(1);
R2 = 0;
}
}
CLK
6 cycles
S
R1
R2
Parallel assignments

## Slide 5: Hardware model behavior

## Slide 6: Reference model-based test oracle
HDL
Test oracle
Reaction
comparators
Reference model
Reaction arbiters
Input interface adapters
Output interface adapters
Stimuli
HDL-model
reactions
Reference model
reactions

## Slide 7: Behavior correctness checking
Time restrictions
Functional properties
Set of reactions is correct
Each reaction is correct
Reaction order is correct
Delays between reactions are correct

## Slide 8: Cycle-accurate checking
R1
Reactions of HDL-model
Reference model reactions
send(R1);
send(R2);
delay(3)
R1
R2

✕
Comparison
R2

✕
3 cycles

## Slide 9: Ambiguity in reaction order
S
R2
R1
Execution of HDL-model
recv(in_iface, S);
Execution of reference model
send(out_iface, R1);
send(out_iface, R2);
...
...
Error: R2  R1
Reverse order
Reaction order
R1
R2
Allowed: R2  Order

## Slide 10: Arbitration of reactions
Reaction arbiter finds a reaction corresponding to the reference model one
Behavior checking depends on both reference model and on arbitration
Reaction arbiters encapsulate parts of test oracle functionality aimed at reaction order checking

## Slide 11: Types of reaction arbiters
Deterministic model-based arbiter
arbiter: 2Reaction  Reaction  {fail}
Adaptive arbiter
arbiter: 2Reaction Reaction  Reaction  {fail}
Two-level arbiter
arbiter(reactions)  arbiter2(arbiter1(reactions), reaction)
  Non-deterministic arbiter
  Adaptive arbiter

## Slide 12: Deterministic arbiter
R1
HDL-model reactions
Reference model reactions
send(R1);
send(R2);
...
R1
R2
Reaction
arbiter
R1
R2
FIFO

✕
Comparison
S
R
Known order

## Slide 13: Adaptive arbiter
R1
HDL-model reactions
Reference model reactions
send(R1);
send(R2);
...
R1
R2
Reaction
arbiter
R1
R2
Get(R1)
Comparison
S
R
Unknown order
Hint

✕

## Slide 14: Two-level arbiter
R1
HDL-model reactions
Reference model reactions
send(R1);
send(R2);
...
R1
R2
Arbiter
#1
R1
R2

✕
Get(R1)
Comparison
S
R
Partially known order
Arbiter
#2
Hint
Candidates

## Slide 15: Timed word (Alur & Dill, 1994)
 – alphabet of events
T – time domain (R≥0 or N)
w = (a0, t0)(a1, t1), …  (  T)(*)
i . ti < ti+1 (ti ≤ ti+1) – monotonicity
T i . ti > T – progress (if |w| = )

## Slide 16: Mazurkiewicz trace (1977)
 – alphabet of events
I   – relation of independence
Equivalent: u  v  u is derived from v by means of reordering of closest independence events
Trace is a class of equivalence of event chains in respect to equivalent relation 

## Slide 17: Mazurkiewicz trace (1977) - Example
 = { a,b,c,d }
I = { (a,b), (c,d) + symmetry}
[ab] = { ab, ba }
[bc] = { bc }
[abcd] = { abcd, bacd, abdc, badc }

## Slide 18: Partially ordered set – Pratt (1982)
 – alphabet of events
Pomset is tuple V, , 
V – set of vertexes
  VV – partial set
: V   – labeling function

## Slide 19: Partially ordered set – Pratt (1982) Examples

## Slide 20: Timed trace – Chieu & Hung (2012)
 – alphabet of events, T – time domain
Timed trace – V, , ,  [, ]
V – set of vertexes
  VV – partial order
: V   – labeling function
: V  T – time of event
: V  T – allowed interval

## Slide 21: Timed trace – Chieu & Hung (2012) Examples
{ abcd, bacd, abdc, badc }
{ abcd, bacd } – time restrictions

## Slide 22: Behavior of specification and implementation
Implementation behavior
VI, , I, I
Specification behavior
VS, , S, S, S
Allowed time interval
S(x) = [S(x)-t(x), S(x)+t(x)]
Correspondence of events
match(x, y) = (I(y) = S(x)) & (I(y)  S(x))

## Slide 23: Conformance relation
I ~ S  t T .
M  { (x, y)pastS(t)  pastI(t) | match(x, y) }
M – one-to-one relation
xpastS(t-t) ypastI(t) . (x, y)M
ypastI(t-t) xpastS(t) . (x, y)M
(x, y), (x’, y’) M . x  x’  (y)  (y’)

## Slide 24: Reaction arbiters
Место для формулы.

## Slide 25: Conformance relation checking

## Slide 26: C++TESK Testing ToolKit
Web: http://forge.ispras.ru/projects/cpptesk-toolkit
E-mail: cpptesk-support@ispras.ru

## Slide 27: Conclusion
Based on the theory of traces and partially ordered multisets method of on-the-fly analysis of hardware systems has been developed
The method has been implemented in C++TESK Testing ToolKit and has been successfully used in a number of projects
Future research is connected with failure diagnostics: giving hints to localization of bugs

## Slide 28: THANK YOU
Any questions?